ROOM PREPARATION – HEIGHT-ADJUSTABLE BATHS

- Electrics

A 4A waterproofed fused spur power supply is required and should be positioned approximately 200mm up from the floor and within 150mm of the end or back of the bath.

If a Spa System, Lights or Audio System is to be included on the bath, an additional fused spur is required.

- Plumbing – Passing Through End Panel

Hot and cold 22mm ball pipe isolation valves are required. Their centres should be situated approx 90mm and 120mm in from the back of the bath, to enable them to be connected through the service entry points in the end panel.

The centre of the 40mm waste pipe should be approx 110mm in from the front of the bath and no more than 75mm off the ground.

- Plumbing – Through Floor

The centres of the 22mm hot and cold pipes to be approx 180mm in from the end of bath, one of them 230mm and the other 270mm in from the back of the bath.

The centre of the 40mm waste pipe to be 220mm in from the end of bath and 250mm in from the front.

- Flooring

Floors must be strong enough to take the weight of the bath + person + water (up to 400kg) and be capable of accepting 75mm fixings up to 280mm in from each end of the bath.

- Wall Clearance

It is recommended that the bath is at least 50mm off the wall for End Panels and 250mm for Side Panels, to allow free movement of the bath up and down and for access to fix the panels to the bath. However, if space is at a premium and if the back and end panels can be fitted before the bath is moved into place, these dimensions can be reduced.